# STM32-ETH Requirements

- Mechanical connect to the two PMOD connectors on ZED
- Power – jumper select from PMOD or local PSU
- Local PSU 3.3V step-down from 12V
- Crystal 25MHz
- STM32F107, LQFP64
- Reset button
- User button
- User LED
- Power-on LED
- PMOD0 – Ethernet RMII via 22R
- PMOD1 – SPI/GPIO, ETH SMI (MDC, MDIO)
- PMOD0,1 – ready for RGMII
- STM MCO pin – via 0R to RMII Clock
- UART connector, 3V3 levels
- JTAG/SWD for STLINK/V2
- All GPIO on pin header
- USB connector
- Screws